KW-4B、KW-4B-I型匀胶机

# 名称：KW-4B、KW-4B-I型匀胶机；                        品牌：北京赛德凯斯；

厂家：北京赛德凯斯电子有限责任公司；      公司网址：www.setcas.com

# KW-4B系列匀胶机(自动型)

| 型号 | 参数 |
| --- | --- |
| KW-4B型匀胶机 全机身采用SUS304不锈钢，防酸、防碱、防盐雾 KW-4B-I型匀胶机 吸附力可调，带真空压力表头实时显示真空吸附状态 | 1、调速范围和匀胶时间 |
|  | Ⅰ档 调速范围：50-10000转／分 Ⅰ档 匀胶时间：0-999秒 |
|  | Ⅱ档 调速范围：50-10000转／分 Ⅱ档 匀胶时间：0-999秒 |
|  | 2、适用：Φ5-Φ120mm硅片及其它材料等匀胶。 |
|  | 3、双LED数字显示，带倒计时显示功能，采用闭环调节方式，转速稳定度：±0.5％，胶的均匀性：±1％。 |
|  | 4、单按键控制电机启动，暂停，复位，单片机延时控制电磁阀启动与停止。 |
|  | 5、电机功率：40W，单相100-250V供电 |
|  | 6、真空泵抽气速率≥60升／分 |
|  | 7、全机身采用不锈钢材质，防酸，防碱，防盐雾 |
|  | 8、仪器尺寸：210×220×160mm |

KW-4B/KW-4B-I Spin Coater:

| MODEL NO. | SPECIFICATIONS: |
| --- | --- |
| KW-4B Spin Coater Made of SUS304 stainless steel, anti-acid, anti-alkali, anti-salt spray KW-4B-I Spin Coater The adsorption force is adjustable, with a vacuum pressure gauge head to display the vacuum adsorption status in real time | 1. Speed range and glue mixing time |
|  | Lower-speed range : 50-10000rpm, Time range : 0-999S |
|  | High-speed range : 50-10000rpm, Time range : 0-999S |
|  | 2. Suitable for ：Φ5-Φ120mm silicon wafer and other material |
|  | Dual LED digital display with countdown display function, Closed-loop regulation，Motor speed stability：±0.5％，glue uniformity：±1％。 |
|  | Single button control motor start, pause, reset, micro Controller delay control solenoid valve start and stop end |
|  | 5. Spin Coater power ：40W，Voltage 100-250V |
|  | 6. Pumping speed ≥ 60L / MIN |
|  | 7. Made of stainless steel, which is acid-proof, alkali-proof and salt-proof |
|  | 8、Dimension：210mm (W) × 220mm (D) ×160mm (H) |